## Slide 1: ENWL’s updated cost performance under Ofgem’s RIIO-ED1 cost assessment methodology
Prepared for
Electricity North West Limited
November 2021

## Slide 2
Overview
Executive summary
Background
Top-down TOTEX models
Bottom-up TOTEX models
Appendix
  Glossary of terms
  ED1 framework summary

## Slide 3
1. Executive summary

## Slide 4: Executive summary Scope of work
in 2020, Electricity North West Limited (ENWL) commissioned Oxera to update the cost assessment models that Ofgem used to set allowances for RIIO-ED1 (ED1) with the latest outturn data at the time (up to 2018/19)
  this output was published alongside ENWL’s draft business plan for RIIO-ED2 (ED2)
ENWL has subsequently commissioned Oxera to update this analysis with additional outturn data up to 2020/21
  in contrast to the previous study, we have access to cost and output data for all companies (based on information shared by ENWL under legal privilege)
the scope is refined to focus on the top-down and bottom-up TOTEX regression models, and sensitivities regarding the analysis period and application of regional adjustments
as in our 2020 study, we do not have access to the analysis files for the ED1 Final Determination (FD), so we focus on the equivalent analysis from the ED1 Draft Determination (DD)
  we compare our updated analysis to that at the Draft Determination

## Slide 5: Executive summary Main conclusions
The quality of the cost models (e.g. in terms of a model’s explanatory power and statistical significance) generally deteriorates with the data updates
4
ENWL continues to perform better in models where regional adjustments are not applied to the data
3
ENWL typically maintains its efficient position (relative to the upper-quartile benchmark) when ED1 models are updated with the latest data
1
In the models where ENWL is ranked outside of the upper quartile, it has a small efficiency gap (c. 0–2%)
2

## Slide 6
2. Background and methodology

## Slide 7: Background Description of the work undertaken
the primary scope of the work is to update the ED1 top-down and bottom-up TOTEX models with the latest outturn data (up to 2020/21)
we also test sensitivities with respect to the following two modelling decisions
Time period of analysis
test the sensitivity of Ofgem’s models and ENWL’s performance to changes to the modelling period
here, we focus on the use of ED1 outturn (2016–21) data and test the full ED1 dataset (2016–23) as a sensitivity (noting that this includes forecast data)
Application of regional adjustments
testing the applications of the pre-modelling adjustments and sensitivity of ENWL’s performance to these

## Slide 8: Background Ofgem’s ED1 regression framework
Ofgem used pooled ordinary least squares (OLS) with a time trend to estimate the regressions of general form:
where is the TOTEX predicted by , the explanatory variables (i.e. the CSV for a regression), and , the time trend. The modelled TOTEX and explanatory variables are logged.
Model | Dependent variable | Explanatory variable
Top-down TOTEX | TOTEX | MACRO_CSV
Bottom-up TOTEX | TOTEX | BU_CSV

## Slide 9: Background Triangulation of the TOTEX modelling outputs
Ofgem triangulated the cost predictions from multiple modelling approaches to derive an overall TOTEX prediction, on which the upper-quartile benchmark was determined
Ofgem indicated that the weight applied to each approach was informed by its confidence in the underpinning data and models
at the fast-track stage, Ofgem gave less weight to the TOTEX models as it noted that it had greater confidence in the disaggregated analysis
at the slow-track stage, Ofgem gave equal weight to the TOTEX models and disaggregated analysis due to its improved confidence in the TOTEX data and models
Triangulated TOTEX
Top-down TOTEX model
Bottom-up TOTEX model
Disaggregated activity based model that involved regression and unit cost analysis, and engineering technical assessments
25%
25%
50%

## Slide 10: Background Ofgem’s pre-modelling regional adjustments to the data
Regional labour costs
real wages (i.e. labour input prices) can differ across regions of GB and are largely exogenous to the DNO
in ED1, Ofgem used the ASHE dataset to calculate a DNO-specific index, assuming that wages differed across three regions: London, South East England, and the rest of GB
Company-specific factors
there may be DNO-specific factors that cause its costs to be higher that cannot be sufficiently captured in the econometric modelling
Ofgem made adjustments for three DNOs, which largely correlated with density and sparsity
Ofgem made pre-modelling adjustments to DNOs’ TOTEX data to reflect differences in labour costs and company-specific factors (collectively ‘regional adjustments’) over and above the factors that were directly included in the model
Ofgem made other adjustments to the data, such as excluding cost items outside of the price control, which are not examined in this study
The regional adjustments in ED1 were taken as given for this project. We note that the use of pre-modelling adjustments may change in ED2, in line with arguments made by some companies at cost assessment working groups and evidence submitted by companies as part of their ED2 business plans.

## Slide 11: Background Additional considerations
Data
the ‘ENA study’ identified some potential inconsistencies in the data from Cost and Volumes reporting packs, and adjusting the data had a material impact on the cost performance of some DNOs
Model specification
we focus on Ofgem’s ED1 model specifications and do not undertake any model development or explore alternative estimation approaches
the ENA study identified areas where the ED1 specifications might be insufficient for assessing ED2 expenditure
Triangulating outcomes
the analysis assesses ENWL’s performance in individual models and does not triangulate across models
as a DNO’s performance could differ across sensible alternative models, triangulation should be considered to assess DNOs’ overall performance
Oxera undertook a cost-driver analysis on behalf of the Energy Networks Association (the ‘ENA study’) that looked into identifying relevant cost drivers for ED2 including the relevance of the ED1 cost models for assessing ED2 expenditure requirements, and highlighted several areas requiring further work, including:
data collection, validation and standardisation;
application of regional wage and density adjustments;
cost driver construction, model specification and validation of outcomes, and so on.
In this output, where appropriate, we comment on the consistency of the insights between the two studies.

## Slide 12
3. Top-down TOTEX models

## Slide 13: Top-down TOTEX models Updated econometric models
 | Top-down ED1 DD | Data update (2020) | Data update (2021)
MACRO_CSV | 0.810*** | 0.795*** | 0.720***
Constant | 23.96*** | 25.72*** | 7.97
Year | -0.0156*** | -0.0164*** | -0.01
Adjusted R-squared | 0.879 | 0.828 | 0.808
Skew/Kurtosis test for normality | 0.08 | 0.18 | 0.22
RESET (functional form) | 0.51 | 0.47 | 0.43
RESET (alternative) | 0.13 | 0.55 | 0.34
White Heteroskedasticity | 0.02 | 0.05 | 0.01
Pooling (F-test) | 0.94 | 0.83 | 1.00
Breusch-Pagan Test | 0.00 | 0.00 | 0.00
Efficiency range | 90–114% | 91–117% | 86–119%
Upper quartile | 95% | 93% | 93%
The estimated coefficient on the CSV falls further with the latest data update, indicating that economies of scale are more pronounced
The R2 also falls further, meaning that the model is less able to explain cost variations with the updated data compared to the DD
The other statistical diagnostics are largely insensitive to the data update
The results presented here are directionally consistent with what was presented in Oxera’s ED2 cost driver study for the ENA and CEPA’s cost assessment working group presentation i.e. model fit worsens with the new data.

## Slide 14: Top-down TOTEX models ENWL’s performance with the updated data
ENWL’s ranking reduces from second at slow-track DD to fourth with the new data
this could be driven by a few factors, including:
  scale economies are slightly more pronounced following the update which may penalise ENWL over smaller DNOs
  ENWL’s MEAV falls in 2020 leading to a decline in its MACRO_CSV
1
3
5
7
9
11
13
Ranking
Note: Efficiency is assessed over the ED1 outturn period (2016–21). Efficiency scores are estimated before reversing the pre-modelling adjustments, in line with the approach taken at ED1. See Ofgem (2014), ‘RIIO-ED1: Final determinations for the slowtrack electricity distribution companies Business plan expenditure assessment’, November, Figure 3.1.

## Slide 15: Top-down TOTEX models ENWL’s performance in additional sensitivities
Time period | Regional adjustments | Ranking | Efficiency | UQ Efficiency
ED1 outturn (2016–21) | With adjustments | 4 | 93% | 93%
ED1 outturn (2016–21) | Without adjustments | 2 | 89% | 91%
ED1 total (2016–23) | With adjustments | 7 | 96% | 94%
ED1 total (2016–23) | Without adjustments | 5 | 91% | 91%
ENWL’s efficiency score is sensitive to the time period of analysis and the application of regional adjustments
ENWL performs best when regional adjustments are not made to the cost data and when the analysis period is limited to outturn data only
where ENWL is ranked lower than the upper-quartile, the gap is relatively small (c. 0–2%)

## Slide 16
4. Bottom-up TOTEX models

## Slide 17: Bottom-up TOTEX models Updated econometric models
 | Bottom-up ED1 DD | Data update (2020) | Data update (2021)
BU_CSV | 0.847*** | 0.807*** | 0.784***
Constant | 28.44*** | 29.92*** | 11.70
Year | -0.0137*** | -0.0143*** | -0.01
Adjusted R-squared | 0.889 | 0.838 | 0.850
Skew/Kurtosis test for normality | 0.11 | 0.22 | 0.43
RESET (functional form) | 0.47 | 0.75 | 0.30
RESET (alternative) | 0.10 | 0.54 | 0.21
White Heteroskedasticity | 0.01 | 0.07 | 0.00
Pooling (F-test) | 0.96 | 0.85 | 1.00
Breusch-Pagan Test | 0.00 | 0.00 | 0.00
Efficiency range | 90–111% | 90–113% | 89–116%
Upper quartile | 95% | 94% | 95%
The estimated coefficient on the CSV falls, indicating that economies of scale are more pronounced
The R2 falls slightly (although by less than with the previous data update), meaning that the model is less able to explain cost variations with the updated data compared to the DD
The other statistical diagnostics are largely insensitive to the data update
The reduction in model explanatory power is consistent with other recent studies examining the performance of the ED1 cost models with the latest data.

## Slide 18: Bottom-up TOTEX models ENWL’s performance with the updated data
ENWL’s ranking improves from fifth at slow-track DD to fourth with the new data
ENWL’s performance is relatively stable, compared to some other DNOs
  the second most efficient DNO currently was less efficient than the lower quartile at the ED1 draft determination
  two of the DNOs that were in the upper quartile at ED1 are now close to average efficiency or lower
1
3
5
7
9
11
13
Ranking
Note: Efficiency is assessed over the ED1 outturn period (2016–21). Efficiency scores are estimated before reversing the pre-modelling adjustments, in line with the approach taken at ED1. See Ofgem (2014), ‘RIIO-ED1: Final determinations for the slowtrack electricity distribution companies Business plan expenditure assessment’, November, Figure 3.1.

## Slide 19: Bottom-up TOTEX models ENWL’s performance in alternative model specifications
ENWL performs similarly in the bottom-up models compared to the top-down models
as with the top-down models, ENWL performs better in models that are estimated using outturn data only and models where regional adjustments are not made
where ENWL is ranked lower than the upper-quartile, the gap is relatively small (c. 2%)
Time period | Regional adjustments | Ranking | Efficiency | UQ Efficiency
ED1 outturn (2016–21) | With adjustments | 4 | 95% | 95%
ED1 outturn (2016–21) | Without adjustments | 3 | 91% | 92%
ED1 total (2016–23) | With adjustments | 8 | 98% | 96%
ED1 total (2016–23) | Without adjustments | 4 | 94% | 94%

## Slide 20
Contact:
Dr Srini Parthasarathy +44 (0) 20 7776 6612 srini.parthasarathy@oxera.com
Oxera Consulting LLP is a limited liability partnership registered in England no. OC392464, registered office: Park Central, 40/41 Park End Street, Oxford OX1 1JD, UK; in Belgium, no. 0651 990 151, branch office: Avenue Louise 81, 1050 Brussels, Belgium; and in Italy, REA no. RM - 1530473, branch office: Via delle Quattro Fontane 15, 00184 Rome, Italy. Oxera Consulting (France) LLP, a French branch, registered office: 60 Avenue Charles de Gaulle, CS 60016, 92573 Neuilly-sur-Seine, France and registered in Nanterre, RCS no. 844 900 407 00025. Oxera Consulting (Netherlands) LLP, a Dutch branch, registered office: Strawinskylaan 3051, 1077 ZX Amsterdam, The Netherlands and registered in Amsterdam, KvK no. 72446218. Oxera Consulting GmbH is registered in Germany, no. HRB 148781 B (Local Court of Charlottenburg), registered office: Rahel-Hirsch-Straße 10, Berlin 10557, Germany.
Although every effort has been made to ensure the accuracy of the material and the integrity of the analysis presented herein, Oxera accepts no liability for any actions taken on the basis of its contents.
No Oxera entity is either authorised or regulated by any Financial Authority or Regulation within any of the countries within which it operates or provides services. Anyone considering a specific investment should consult their own broker or other investment adviser. Oxera accepts no liability for any specific investment decision, which must be at the investor’s own risk.
© Oxera 2021. All rights reserved. Except for the quotation of short passages for the purposes of criticism or review, no part may be used or reproduced without permission.
www.oxera.com Follow us on Twitter @OxeraConsulting

## Slide 21
Appendix
Glossary
ED1 summary

## Slide 22
Appendix i: glossary

## Slide 23: Glossary of terms General concepts
Term | Definition
ED1 | RIIO-ED1 or ED1 is the current price control (2016–23).
ED2 | RIIO-ED2, or ED2 is the upcoming price control (2024–28).
Cost function | The cost function is the mathematical formula that describes how expenditure is related to structural factors (e.g. scale) and other drivers of costs (e.g. operating environment).
OLS | Ordinary Least Squares (OLS) is an econometric method used to estimate the relationship between a dependent variable (e.g. TOTEX), and one or more independent variables (e.g. cost drivers). This was the method used by Ofgem to estimate cost functions in ED1.
POLS | Pooled OLS (POLS) is a method of performing regression that assumes that a DNO’s costs in a given time period are independent of their costs in another time period.
RE | Random Effects (RE) is a method of performing regression assumes that accounts for the panel structure of the data (i.e. the fact that the sample is not entirely independent but consists of observations for a set of companies over time).
Efficiency | In this context, the efficiency of a company represents the ability of a company to transform inputs into outputs relative to best practice. The efficiency of a company is an unknown that must be inferred (or estimated) from the modelling. In Ofgem’s approach, estimated efficiency refers to the ratio between a company’s observed expenditure and that predicted by a model (so smaller the ratio, higher is the estimated efficiency of a DNO).
TOTEX | TOTEX excluding certain costs (as defined at ED1).
MEAV | Modern Equivalent Asset Value (MEAV) is defined as the weighted sum of DNOs’ assets, where the weights are derived from engineering assessments. MEAV was used a cost driver for the ED1 determination.
BU_CSV | Units distributed, total network length, LV and HV overhead line length, MEAV, spans cut, total faults, and total ONIs, weighted by industry spend.
MACRO_CSV | Combination (i.e. composite scale variable, CSV) of the number of customers and MEAV.

## Slide 24: Glossary of terms Statistical diagnostics
Term | Description
R-Squared | R-Squared (R2) is a measure of model fit, and is defined as the proportion of the variance in expenditure that can be explained by the variance in the cost drivers. In other words, it is a measure of how well the cost drivers can explain differences in costs over the modelled period. If a model fits the data poorly (i.e. a low R2), it might exclude relevant cost drivers. Under Ofgem’s approach, this could risk conflating the impact of omitted factors with inefficiency. Conversely, ‘overfitting’ the model (i.e. seeking a high R2) can result in unnecessary, counterintuitive and incorrect parameter estimates.
Adjusted R-squared | Adjusted R2 is a measure of model fit, where there are penalties associated with adding cost drivers. It is intended to account for potential ‘overfitting’.
Skew\Kurtosis test for normality | The Skewness and Kurtosis test (SK-test) is a test for whether a given variable follows a normal distribution. In this context, it is applied to the residuals of the model (i.e. difference between predicted and actual costs). If the residuals are not normally distributed, then many of the statistical tests considered by Ofgem may not provide valid inference.
RESET | The Ramsey Regression Equation Specification Error Test (RESET) test is a test for model misspecification. It is intended to identify whether non-linear relationships (e.g. squared terms) exist in the data.
RESET (alternative) | This is a slight variant of the RESET test applied by Ofgem that looks at higher order non-linear relationships (e.g. quadratic, cubic and quartic functions).
White Test | The White Test is intended to detect the presence of heteroskedasticity, the phenomenon whereby the variance of the residual is correlated with the cost drivers. If heteroskedasticity is present, the standard errors on the coefficients will be biased and statistical tests will be uninformative.
Pooling (F-test) | The Pooling (F-test) is intended to detect whether the coefficients on the cost drivers are stable over time. If the coefficients are unstable, then it might not be appropriate to pool the data.
Breusch-Pagan test | The Breusch-Pagan test is intended to detected whether POLS or RE is the more appropriate estimation approach.

## Slide 25
2. Appendix ii: ED1 framework Summary

## Slide 26: Overview of Ofgem’s RIIO-ED1 cost assessment approach
Triangulation of model outputs
Pre-regression adjustments
Regression estimation
Post-regression adjustments
Application of Upper Quartile
Smart Grids and RPEs
Interpolation of Ofgem: DNO view

## Slide 27: Regression results Example regression results from ED1 Determinations
Variable | Top-down (DD) | Bottom-up (DD) | Top-down (FD) | Bottom-up (FD)
BU_CSV |  | 0.847*** |  | 0.827***
MACRO_CSV | 0.810*** |  | 0.788*** | 
year | -0.0156*** | -0.0137*** | -0.0144*** | -0.0127***
Constant | 23.96*** | 28.44*** | 22.01*** | 26.65***
Adj. R-Squared | 0.88 | 0.89 | 0.87 | 0.88
Source: Ofgem (2014), ‘RIIO-ED1: Draft determinations for the slowtrack electricity distribution companies: Business plan expenditure assessment’, July, pp. 156–158; Ofgem (2014), ‘RIIO-ED1: Final determinations for the slowtrack electricity distribution companies: Business plan expenditure assessment’, November, pp. 193–195.

## Slide 28: ENWL’s overall position at ED1 slow-track final determination
Fast-track | DD | FD
SWALES | SPD | ENWL
WMID | ENWL | SPD
EMID | SSES | SSES
SSES | EMID | SWALES
SWEST | NPgY | EMID
ENWL | SWALES | NPgY
SSEH | SPN | SSEH
NPgN | EPN | NPgN
SPN | NPgN | SPN
NPgY | SSEH | EPN
SPD | WMID | LPN
LPN | LPN | WMID
EPN | SPMW | SWEST
SPMW | SWEST | SPMW
ENWL was below UQ at the fast-track stage
at FD, ENWL was the top-ranked (frontier) DNO
this ranking reflects TOTEX adjusted for Smart Grid benefits and RPEs
cost benchmarking occurs ‘before’ the adjustments for Smart Grids and RPEs
the results on the next slide cover only the contribution of the cost benchmarking (before the reversal of pre-modelling adjustments) to ENWL’s ranking at DD and FD

## Slide 29: Results of regression performance in ED1 ENWL was in or close to the upper-quartile in ED1
DNO | Bottom-up DD | Top-down DD | Bottom-up FD | Top-down FD
ENWL | 5 | 2 | 5 | 2
NPGN | 8 | 8 | 7 | 7
NPGY | 3 | 4 | 6 | 6
WMID | 12 | 12 | 9 | 10
EMID | 10 | 9 | 4 | 3
SWALES | 6 | 7 | 3 | 4
SWEST | 14 | 14 | 13 | 13
LPN | 9 | 6 | 12 | 9
SPN | 2 | 1 | 8 | 8
EPN | 7 | 10 | 10 | 12
SPD | 4 | 3 | 1 | 1
SPMW | 13 | 13 | 14 | 14
SSEH | 11 | 11 | 11 | 11
SSES | 1 | 5 | 2 | 5